## Slide 1
A Multimodal
Attention Tracking
in HRI for Industrial Robots in tasks
Robot is able to track operator’s attention through the vision and oral input during the HRI.

## Slide 2
https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.pinterest.dk%2Fpin%2F63191201000733517%2F&psig=AOvVaw3opz-MQ_7thWgK4wXyb635&ust=1615905908680000&source=images&cd=vfe&ved=
Franka Robot
Workflow
Operator
Max
Camera
DB or Script run in Max
Oral instruction
Response
Visual information of the Operator’s eyes/head position
Attention Tracking
NN for Conversation
NN for Vision
Action Selection
Action/State
…
Assembly Tasks
Max will keep tracking the operator’s attention by analyzing what operator says.
Max will keep tracking the operator’s attention by monitoring operator’s head and eye movement.

## Slide 3
Operator
Action: Speak
Action: Movement
Action: Co-Assembly
Non-task related conversation
Task-related oral command
Eye movement
Head position
Body gesture
Lego
Phone
TBC
Hey Franka, how are you doing?
Can you start to assembly?
example
example
Need to discuss
Which task it can work on?
Operator changes gazing direction
example
Operator move head away
example
Input of Max
Input of Max
Need to discuss
where should the camera be installed
Actor

## Slide 4
Input of Franka
Max
Action: Understand
Recognize the operator’s intent
Recognize the command
Action: Monitor
Tracking the operator’s intent
Analyzing the dialogue context
Tracking the operator’s eye/head
Action: Generate Action
Generate the Cov. Response
Send the command to the robot
Actor
Need to discuss
Grounding intents
Need to discuss
Grounding robot skills
Max verifies if what operator says makes sense or not.
Need to discuss
the communication between Max and Franka , as well as the data format
Sure, l will do the assembly now.
example
Max monitors the change of the eye and head position of the operator

## Slide 5
Input of Max
Franka Robot
Action: Query/Mapping
Action: Update
Action: Co-Assembly
Query the oral instruction
Grounding the oral command
Update the state of the task
Report the state of the system
Lego
Phone
TBC
Actor
Need to define the states and the data format

## Slide 6: Demo – previous work
Clip two: head pose change
Clip one: Intent switch
Description: tracking the attention by monitoring the intent switching
Description: tracking the attention by monitoring the head pose

## Slide 7: Case – Phone Assembly (1)

## Slide 8: Scenario Description
Dummy Mobile Phone
Parts
  Top Cover
  PCB
  Fuses
  Bottom Cover
Feature
  Color of Cover
    White
    Blue
    Black

## Slide 9: Scenario Description
Assembly Tasks
  Task one:
    FE helps operator to assembly phone
      Focus on - bring part to the operator
  Task two (tbc)

## Slide 10: Scenario Description
FE Skill
  Grasp part (fix location)
  Deliver part (fix location)
  Other
    Report task state
    Pause/Continue task
Model Capability
  Vision
    Identify category ()
    Location (?)
    Recognize color
  Language
    Recognize Intent
    Infer command

## Slide 11: Task related Built-in Intents
TaskCheck
Example utterances
Hey, what are you working on?
Hey, are you free now?
BringPart
Max, give a white bottom cover.
Max, I need a fuses please
Max, can you grasp a PCB for me?
Intents
PauseTask
Max, please wait for a second.
Stop right now, please.
Hold on a second
ContinueTask
Max, please continue.
Ok, let’s start it.
Max, keep working

## Slide 12: Example Scenario
Hey Max, please give me a fuses.
1
2
Sure, give me a second.
Basic Assembly
3
Here you are.
Thanks!
4
Intent: BringPart
Object: fuses
Color: None
Action
Object identification
Grasp
Action
Deliver

## Slide 13: Example Scenario
Hey Max, please give me a cover.
1
2
Sure, but which color you need.
Attention based Assembly
Sorry, do you still need me to give you a cover?
Yes, give me the blue cover first. Thanks.
5
Intent: BringPart
Object: cover
Color: None
Action
pausetask
I need a fuses please.
3
Intent: BringPart
Object: fuses
Color: None
4
Intent: BringPart
Object: cover
Color: blue
6
Action
Object identification
Grasp
Deliver
Here you are.

## Slide 14: Tasks